## Slide 1
2F. Universal Logic

## Slide 2
FPGAs
Inside FPGA  Each
‘universal Logic Function’ has two aspects:
Programmable logic block (PLB)
Programmable interconnect
their underlying fabric predominantly consists of large numbers of relatively simple programmable logic block “ islands ” embedded in a “ sea ” of programmable interconnect
Programmable logic block
Coarse-grained Architecture
Fine-grained Architecture
(universal gates like NAND, NOR)
Medium-grained Architecture
MUX/LUT
Configurability increases
Denser interconnect
Configurability decreases
Sparser interconnects

## Slide 3
Medium Grained Architecture
each input to the block is presented with a 0, a 1, or the true or inverse version of a signal ( a , b , or c in this case) coming from another block or from a primary input to the device.
MUX approach
MUXes can be supplemented with registers to store a, b. Depending on the function, we update these. So while the MUX config is fixed, you can reprogram the inputs to get different outputs.

## Slide 4
Medium Grained Architecture
A group of input signals  index (pointer) to a lookup table.
The contents of this table are arranged such that the cell pointed to by each input combination contains the desired value.
LUT approach
To implement:
load a 3-input LUT with the appropriate values into SRAM

## Slide 5
MUX vs LUT
LUT PROs
LUT CONs
large complex circuit of logic gates  very efficient in terms of resource utilization and input-to-output delays (parallel)
MUX PROs
MUX CONs
intermediate values are accessible from the signals linking the logic gates and the MUXes.
MUX logic chain  carry logic becomes slow
to implement a small function(2-input AND gate), you’ll end up using an entire LUT to do so  wasteful
A LUT can be reconfigured to be used as RAM if needed

## Slide 6
Coarse Grained Architecture
Each block has its own little LUT, some RAM, a few MUXes etc.
You have logic blocks/cells
They can also have dedicated multipliers/adders in each cell
Even a small microprocessor!
NOT DISCUSSED HERE:
Clock tree managers(manage all timing signals)
Softcore processors
Configurable I/O
IP(intellectual property) cores and their uses

## Slide 7
Processors: AND/OR
Selectors: MUX/DEMUX, Encoders
Clocks: Shift Registers
Memory: Flip-Flops/Registers
In summary

## Slide 8
Next Lecture
How we add quickly
(Intro to CMOS)