## Slide 1
Fundamentals of Computing
Lec 2
How we add

## Slide 2
Digital Computing in Silico
How we compute (algorithms)
How we add (Gates)
How we add quickly (CMOS)
Energy cost
How we fix errors
Overall structure of this course
Analog Computing in Carbo
How we train (Supervision)
Physics of Neurons (Boltzmann)
How we learn (time sampling)
Optimizing and Classifying
Transition Theory & Inferencing
Quantum Computing in Magneto
Quantum Spins and Hardware
Quantum Physics
Entanglement and Superposition
Quantum Search and Annealing
Quantum Gates and Factorization

## Slide 4
W.x
How to add?
Synapse
Neuron

## Slide 5
2A. Elementary gates for addition

## Slide 6
1. Encoder
9  1001, 5 0101
2. Processor
Col1: 9 + 5 = 14 (store 4 carry 1)
Col2: 9 + 5 = 14 + 1 = 15
Answer: 154  10011010
3. Decoder
10011010  154
4. Memory
Instruction sets (how to add), address, data upload/download
5. Clocks for synchronizing
6. Multiplexers for routing and Programmable Logic
99 + 55 = ?
99
+ 55
154
1
1

## Slide 7
To control these operations,
we need gates

## Slide 8
Simple gate: an inverter
1-input 1-output
NOT
0
1
1
0
in
out
out
in

## Slide 9
0
0
0
0
1
0
1
0
0
1
1
1
2-input Logic Gates
0
0
0
0
1
1
1
0
1
1
1
1
AND
OR
A
B
A⋂B
A
B
A ⋂ B
A
B
A U B
A
B
A U B

## Slide 10
0
0
1
0
1
1
1
0
1
1
1
0
2-input 1-output Logic Gates
0
0
1
0
1
0
1
0
0
1
1
0
NAND (A ⩃ B)
NOR (A ⩂ B)
0
0
0
0
1
1
1
0
1
1
1
0
XOR (A ⨁ B)

## Slide 11
Other Logic Gates
Exchange
Fanout/
Copy

## Slide 12
Quantum Logic Gates
Hadamard
(Quantum Superposition)
Boolean does not allow mixtures
(it’s either-or)

## Slide 13
Quantum Logic Gates

## Slide 14
Quantum Logic Gates

## Slide 15
Classical Logic Gates

## Slide 16
Quantum Logic Gates
Hadamard
(Quantum Superposition)
Boolean does not allow mixtures
(it’s either-or)

## Slide 17
Quantum Logic Gates
Hadamard
(Quantum Superposition)
Reversible Gate

## Slide 18
Irreversible gates
It is not reversible because you are
discarding information from input to output !!

## Slide 19
Reversible gates
It is not reversible because you are
discarding information from input to output !!

## Slide 20
How many flavors of logic gates do we need?

## Slide 21
To be Universal
Must block an
input (e.g. A)
Here output ignores A
Only
Dep on
B
A
B = 0 or 1
Must generate
a NOT
A
A

## Slide 22
NAND is universal
NAND
A
B
NOT
A
A
AND = NOT(NAND)
B=0, output = 1 independent of A (blocks A)

## Slide 23
NAND is universal
NAND
A
B
A OR
A
A OR B = [A ⩃ B]
Come Rain or Shine = Not(rainless and shineless)
B
B
A
B

## Slide 24
2B. Binary representation

## Slide 25
Write down truth table
Write in terms of known gates

## Slide 26
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
1
0
0
0
0
0
0
0
0
0
0
1
0
1
2
3
4
5
6
7
8
9

## Slide 27
10 finger counting
1234
= 1 x 103 + 2 x 102 + 3 x 101 + 4 x 100

## Slide 28
(10 finger to 2 finger logic)
7 = 0111
= 0 x 23 + 1 x 22 + 1 x 21 + 1 x 20
5 = 0101
12 = 1100
MATLAB

## Slide 29
10 finger addition
1 2 3 4
+ 2 1 5 7
-----------

## Slide 30
4 Bit Adder
7 = 0 1 1 1
5 = 0 1 0 1
2 = 10
1 0
2 = 10
1 0
3 = 11
1 1
1 = 01
1
12 =

## Slide 31
Half-Adder
CARRY = AND = A ⋂ B
SUM = XOR = A ⨁ B
0
0
0
0
1
0
1
0
0
1
1
1
A
B
A
B
CARRY
SUM
0
1
1
0
0
1
1
2

## Slide 32
Full-Adder
(include previous carry
as extra input)
A
B
Sum
S
Carry
Cout
Cin
Cin | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
S = A + B + Cin
Cout = (A ⋂ B) U (B ⋂ C) U (A ⋂ C)

## Slide 33
2 Bit Adder
CARRY =
(A ⋂ B)U(B ⋂ Cin)U(A ⋂ Cin)
SUM = A XOR B
XOR Ci
A
B
Cin

## Slide 34
32 Bit Adder
+

## Slide 35
https://www.youtube.com/watch?time_continue=818&v=wvJc9CZcvBc&feature=emb_logo

## Slide 36
2C Signed addition (Negative numbers)

## Slide 37
Designate a bit as ‘sign bit’
https://microchipdeveloper.com/lin:protocol-dll-lin-message-frame
28 = 00011100
-28 = 10011100 ????
No because sum does not give 00000000 !!!

## Slide 38
28 = 00011100
TO GET NEGATIVE of ABCDEFGH,
WE NEED TO SUBTRACT FROM 0
00000000
-ABCDEFGH
SINCE WE DROP 9TH BIT, WE MIGHT AS WELL DO
100000000
-ABCDEFGH

## Slide 39
But 100000000
= 11111111 + 1
AND
11111111
-ABCDEFGH
IS SIMPLY FLIPPING DIGITS OF ABCDEFGH
e.g. 1-0 = 1
1-1 = 0

## Slide 40
THUS TWO’S COMPLEMENT: FLIP AND ADD 1
(1st DIGIT 0 means +, 1 means -)
-28 = 11100011+1
= 11100100

## Slide 41
TO READ
Just binary  decimal, except first unit is subtracted
11100100
- 27 x 1 + 26 x 1 + 25 x 1 + 24 x 0 + 23 x 0 + 22 x 1 + 21 x 0 + 20 x 0
= -128 + 64 + 32 + 0 + 0 + 4 + 0 + 0 = -28

## Slide 42
TO FLIP BACK
DO TWOS COMPLEMENT AGAIN
LEFTMOST BIT is still sign
00011011+1
= 00011100

## Slide 43
32 Bit
Signed
Adder

## Slide 44
+
Aside: Digital Multiply
11010
X 1111
-----------
11010
11010
11010
11010
-----------
COPY & SHIFT
101110110

## Slide 45
Multiply
11010
X 1001
-----------
11010
00000
00000
11010
-----------
COPY
+
101110110
NO COPY
In practice, Booth algorithm to minimize copies

## Slide 46
2D.
Interfaces and Routing:
Encoder-Decoder
MUX-DEMUX

## Slide 47
OK, so we know how to add in binary.
But how do we convert between decimal
& binary in the first place?
And how do we send multiple answers
on the same line without blowing up
I/O ports?

## Slide 48
Encoder: 2n inputs, n outputs
Decimal to binary
A
B
D0
D1
D2
D3
Enable
0
1
2
3
0
0
0
1
1
0
1
1
0
1
2
3
0
1
2
3
0
1
2
3
0
1
2
3

## Slide 49
Encoder: 2n inputs, n outputs
A
B
D0
D1
D2
D3
D0 | D1 | D2 | D3 | A | B
1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 1
Enable
A = D2 + D3 = NOT(XOR(D0,D1))
B = D1 + D3
OR GATES

## Slide 50
Decoder: n inputs, 2n outputs
(Assign each 3 bit address to a
different line
e.g. Binary to Decimal)

## Slide 51
Decoder: n inputs, 2n outputs
(Convert Decimal into code
Identifies each A-B possibility)
A
B
D0
D1
D2
D3
A | B | D3 | D2 | D1 | D0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
Enable
D0 = A NOR B = NOT(A) AND NOT(B)
D1 = NOT(A) AND B
D2 = A AND NOT(B)
D3 = A AND B
AND GATES

## Slide 52
Multiple inputs-outputs
(n vs 2n)
Encoders vs Decoders
What if we have only 1 output line?
MUX/DEMUX

## Slide 53
2x1 and 4x1 Multiplexer
(Selector – 1 output)
F
A
B
Control S
S=0, F=A
S=1, F=B
F = S.A + S.B
F
A
B
S0
S1
C
D
(S0,S1) = (0,0), F=A
(0,1), F=B
(1,0), F=C
(1,1), F=D
F = S0.S1.A + S0.S1.B + S0.S1.C + S0.S1.D

## Slide 54
2x1 and 4x1 Multiplexer
(Selector – 1 output)
F
A
B
S0
S1
C
D
F = S0.S1.A + S0.S1.B + S0.S1.C + S0.S1.D

## Slide 55
8 x 1 Multiplexer DEMUX
F
D0
D1
S0
S1
D2
D3
D4
D5
D6
D7
S2
F
D0
D1
S0
S1
D2
D3
D4
D5
D6
D7
S2

## Slide 56
8 x 1 DEMUX

## Slide 57
2N MUX can implement any N input Boolean function
Multiplexer –
3 bit address code decides which input is transmitted

## Slide 58
Universal Logic Function

## Slide 59
Before we see how universal
logic is coded, let’s look at
memory

## Slide 60
2E. Memory

## Slide 61
Odd # NOTs – oscillator; Even = memory
Odd Number with feedback – keeps changing
(Oscillator)
Even Number with feedback - Reaffirms (Memory)
Both need a clock to
control switching

## Slide 62
Memory

## Slide 66
2F. Universal Logic

## Slide 67
FPGAs
Inside FPGA  Each
‘universal Logic Function’ has two aspects:
Programmable logic block (PLB)
Programmable interconnect
their underlying fabric predominantly consists of large numbers of relatively simple programmable logic block “ islands ” embedded in a “ sea ” of programmable interconnect
Programmable logic block
Coarse-grained Architecture
Fine-grained Architecture
(universal gates like NAND, NOR)
Medium-grained Architecture
MUX/LUT
Configurability increases
Denser interconnect
Configurability decreases
Sparser interconnects

## Slide 68
Medium Grained Architecture
each input to the block is presented with a 0, a 1, or the true or inverse version of a signal ( a , b , or c in this case) coming from another block or from a primary input to the device.
MUX approach
MUXes can be supplemented with registers to store a, b. Depending on the function, we update these. So while the MUX config is fixed, you can reprogram the inputs to get different outputs.

## Slide 69
Medium Grained Architecture
A group of input signals  index (pointer) to a lookup table.
The contents of this table are arranged such that the cell pointed to by each input combination contains the desired value.
LUT approach
To implement:
load a 3-input LUT with the appropriate values into SRAM

## Slide 70
MUX vs LUT
LUT PROs
LUT CONs
large complex circuit of logic gates  very efficient in terms of resource utilization and input-to-output delays (parallel)
MUX PROs
MUX CONs
intermediate values are accessible from the signals linking the logic gates and the MUXes.
MUX logic chain  carry logic becomes slow
to implement a small function(2-input AND gate), you’ll end up using an entire LUT to do so  wasteful
A LUT can be reconfigured to be used as RAM if needed

## Slide 71
Coarse Grained Architecture
Each block has its own little LUT, some RAM, a few MUXes etc.
You have logic blocks/cells
They can also have dedicated multipliers/adders in each cell
Even a small microprocessor!
NOT DISCUSSED HERE:
Clock tree managers(manage all timing signals)
Softcore processors
Configurable I/O
IP(intellectual property) cores and their uses

## Slide 72
Processors: AND/OR
Selectors: MUX/DEMUX, Encoders
Clocks: Shift Registers
Memory: Flip-Flops/Registers
In summary

## Slide 73
Next Lecture
How we add quickly
(Intro to CMOS)