## Slide 1
Fundamentals of Computing
Lec 3
How we add quickly

## Slide 2
Digital Computing in Silico
How we compute (algorithms)
How we add (Gates)
How we add quickly (CMOS)
Energy cost
How we fix errors
Overall structure of this course
Analog Computing in Carbo
How we train (Supervision)
Physics of Neurons (Boltzmann)
How we learn (time sampling)
Optimizing and Classifying
Transition Theory & Inferencing
Quantum Computing in Magneto
Quantum Spins and Hardware
Quantum Physics
Entanglement and Superposition
Quantum Search and Annealing
Quantum Gates and Factorization

## Slide 4
Recall Two pieces in ML/AI
Sum
Threshold

## Slide 5
Encode info in binary (BITs):
 18
11011  27
Silicon Brain
We can store 0’s and 1’s as data strings
Logic gates map binary strings between
input and output
AND, XOR: (2 bits  1 bit)
FA: (32+32  33)

## Slide 6
Manipulating these cost energy. How much? Energy loss related with information loss
Silicon Brain
Reduction of entropy consumes energy – Lec 4.

## Slide 7
Encode info in binary (BITs):
Silicon Brain
1 0 0 1 0
1 1 0 1 1

## Slide 8
Instead of mechanical switches, it’s electrical
Silicon Brain
1 0 0 1 0

## Slide 9
I
VSD
OFF “0”
ON “1”
Silicon Brain
Signs flip between PMOS and NMOS

## Slide 10
3A. Intro to CMOS

## Slide 11
Basic NOT gate: an inverter
NOT
0
1
1
0
in
out
out
in
Do billions of this at
High speed (~GHz)
Low power (~mW in IoT, W on cell phones/laptops)
Low dynamic error (~10-12)

## Slide 12
Vout = 0
Vout = V
V
V
Electrical switching
Positive input turns the lower limb (NMOS) on
Negative input turns the upper limb (PMOS) on  Inverter!!

## Slide 13
Complementary Metal Oxide Semiconductor (CMOS)
Vout = 0
V
V
Vout = V
Difference is orders of magnitude !
(resistivity of metals vs oxides ~10-6-1014 W–cm)
One is always off (static dissipation ideally ZERO)

## Slide 14
3B. How does each MOS transistor work?

## Slide 15
Need a Band diagram first

## Slide 16
Electrons form standing waves in a grating
Some wavelengths filtered out
 Energy gaps
E
Gap

## Slide 17
Bands are direction dependent
Chemical orbitals (s,p,d)
Brillouin zone
Valleys and optical activity
Effective mass
Valence Bands and strain
Symmetry and topology
Heterostructures and band splitting
Density of States

## Slide 18
E-k plots carry a lot of information
Optical absorption for direct bands (photons have zero mass and low momentum)
Fit a parabola to get an effective mass
Steeper is lighter (mGaAs < mSi)
Orbital and spin characters control transitions between bands

## Slide 19
Electrons occupy bands based on Pauli exclusion
E
Filled
Empty
Fermi Energy EF
Transition
~25meV
Bandwidth
~5eV
Unavailable
Bandgap
~1 eV

## Slide 20
E
Metal (Copper)
(charges move)
Filled
levels
Empty levels
Insulator (Silica)
(charges can’t move)
Semiconductor (Si)
(charge movement
can be controlled)
Bands determine what kind of solid we have
~10eV
~1eV
1eV = 1.6 x 10-19 J = 1.24/l(mm)

## Slide 21: Act of electronic switching

## Slide 22: In plain English…
Vacuum
Level
VG > 0
n type operation
Positive gate bias attracts electrons into channel
Channel now becomes more conductive
More
electrons

## Slide 23: In plain English…
Vacuum
Level
VG < 0
p type operation
Negative gate bias attracts holes into channel
Channel now becomes more conductive
More
holes

## Slide 24: The origin of high ON-OFF

## Slide 25
What is ‘n’?
Number of ‘free’ electrons in NMOS
(untied to parent)

## Slide 26
There is a corresponding ‘p’
Number of ‘free’ holes in PMOS

## Slide 27
Intrinsic semiconductor

## Slide 28
Create excess electrons and holes by doping
This also moves EF towards CB

## Slide 29
Create electrons and holes by doping
This also moves EF towards VB

## Slide 30
Charges grow at each other’s expense
Arithmetic Mean can change with doping
Geometric Mean stays fixed

## Slide 31
Charges grow at each other’s expense

## Slide 32
Note how voltages are related
to concentration logarithmically
How can we use this?

## Slide 33
3C. Building devices out of this
PN junctions

## Slide 34
P and N together

## Slide 35
P and N together

## Slide 36
P and N together

## Slide 37
P and N together

## Slide 38
Forward Bias – Exponentially grow current

## Slide 39
Reverse bias – Reduce current to saturation

## Slide 40
Barrier Engineering

## Slide 41
Speed of the diode

## Slide 42
Speed of the diode

## Slide 43
Mobility in an electric field

## Slide 44
Diffusion in thermal field

## Slide 45
Electrons in semiconductors are fast because
1. They are light!
2. Less interruptions in a clean solid (low scattering)
lesc ~ 10—100s of nm
(1000x electron size ~0.1 nm)
lH20sc ~ 100 nm
(25x molecule size ~ 4 nm)

## Slide 46
Use for a PN junction: Solar Cell

## Slide 47
Solar Cell

## Slide 48
3D. From single PN junction to MOS
transistor

## Slide 49
Transistor acts like a solar cell
(Inundates with excess charges)

## Slide 50
Transistor acts like a solar cell
(Inundates with excess charges)

## Slide 51
NPN transistor  NMOS transfer characteristic

## Slide 52
PNP transistor  PMOS transfer characteristic

## Slide 53
Drain bias reverse biases one end
(like solar cell)

## Slide 54
Output characteristics

## Slide 55
How do these I-Vs translate to CMOS inverter?
Gain
ON
OFF

## Slide 56
CMOS – Combine NMOS and PMOS

## Slide 57
Short-channel effects

## Slide 58
Build a “NOT” with CMOS inverters
+ voltage turns NMOS on, shorts to
ground
voltage turns
PMOS on, shorts
to power supply voltage
NMOS
PMOS
Gain
ON
OFF

## Slide 59
0
0
1
0
1
1
1
0
1
1
1
0
Build a NAND with CMOS inverters
NAND

## Slide 60
0
0
1
0
1
0
1
0
0
1
1
0
Build a NOR with CMOS inverters
NOR

## Slide 61
Build memory with CMOS
(6T-SRAM)
Cache memory

## Slide 62
Build memory with CMOS
(DRAM)
Main memory: PC, workstations, servers
Slower than SRAM (leakage)
Denser and cheaper

## Slide 63
Memory Sticks, PC cards

## Slide 64
Need rise and fall times of CMOS equal
RPMOS = 2RNMOS
NAND:
2 NMOS in series: R = ?  Pull down
2 PMOS in parallel R = ?  Pull up
Lower resistance
Series connection means stackable, smaller (denser, cheaper)
NOR:
2 NMOS in parallel: R = ?  Pull down
2 PMOS in series: R = ?  Pull up
Higher resistance
Faster to read
(address each bit individually)
Slower to write/erase (erase each to 0
before over-writing)

## Slide 65
Why CMOS specifically for inverters?
Low power: Once settled, no static current flow
~MW
~KW
+V1
V
-V
-V
~MW
~KW
-V1
V
+V
-V

## Slide 66
3E. The trouble with CMOS

## Slide 67
CMOS drove Moore’s Law for decades
Smaller/Faster/Cheaper

## Slide 68
..Trouble in Paradise !
Pentium 2000, 50W/cm2;
~2025, 40MW/cm2
Based on Fundamental considerations alone !

## Slide 69
Dissipation in CMOS
Pdiss ∝ V2 f
Freq & V
Scaling –
Death of Dennard Scaling
Strained
Si
High-K
Metal Gate
NonPlanar
Gate
No More
ITRS roadmap !
3V
2V
1V
Limited by
Error tolerance
Limited by
Heat
V
f
Gordon Moore

## Slide 71
ITRS  IRDS

## Slide 72
To summarize
Electrons in silicon are quick (low mass, clean systems)
~ GHz
They consume low power (CMOS architecture – no static
current), although high dynamic power is now slowing down
further scaling
~mW-W
They are accurate because the barriers (bandgaps) are
very large due to low electron mass, and much bigger than
thermal energy kT which is set by atomic mass and its
sluggish motion
~ 10-12-10-15 dynamic error

## Slide 73
3F. SPICE modeling of circuits

## Slide 74
LAB : COMPUTER MODELING
Drift-Diffusion
Boltzmann Transport NEGF
SPICE

## Slide 75
LTSPICE
Download LTSPICE for MAC-OSX
Install

## Slide 76
Draft  Component  npn
Open Draft --> component to pick a piece

## Slide 77
Replication is automatic with cursor movement
To stop, hit escape
To cancel, fn F5 (scissor comes up, then cut and then esc to stop)
To move, fn F7 then drag and draw box around limb of any subfigure, then move
To flip, click on figure after fn F7, then command E
Duplicate, Erase, Drag, Flip

## Slide 78
Draft  Wires, double click to start, single click to extend, esc to escape
fn G for each ground
Draft  Component  Voltage for V-source, current for current-source
Draw wires, add ground, resistors, voltage/current sources

## Slide 79
Right Click, pulls up sheet for each component
Enter values (e.g. R, V)
Fix NPN features, Voltages, current sources

## Slide 80
For each transistor, right click to pull up transistor data sheet, pick new transistor
CTRL c to copy any of the transistors (first one eg), then cancel
Fix Transistor specs

## Slide 81
Draft SPICE directive then copy Ctrl V info into blank space, then edit
Replace model name with transistor name
Gain (BF), or other info (seek manual)
Fix Transistor specs

## Slide 82
Set voltage conditions for run
[V0, V1 range, V0 start, DV step]
.tran 0 5 0 0.1 (in spice directive)
New window pops up
Bring cursor over wire on main window
Voltage probe (red) pops up
CMD switches to current probe
Graphs shown on output window
Current across top left and top right segments
(Mirror)

## Slide 83
Poor mirror
Current across top left and top right segments
(Mirror)

## Slide 84
Current Mirror works because of the cross link, which allows I1 to control VBE so that Iout equal I1

## Slide 85
CMOS

## Slide 86
Next class
Lec 4
Thermodynamics of Computing