## Slide 1
Fundamentals of Computing
Lec 4
Thermodynamics of
Computing

## Slide 2
Digital Computing in Silico
How we compute (algorithms)
How we add (Gates)
How we add quickly (CMOS)
Thermodynamics of Computing
How we fix errors
Overall structure of this course
Analog Computing in Carbo
How we train (Supervision)
Nature’s Supervision (Boltzmann)
How we learn (time sampling)
Optimizing
Classifying (Truth Tables)
Transition Theory
Inferencing (Bayesian)
Quantum Computing in Magneto
Quantum Spins and Hardware
Interacting Spins
Going parallel: Quantum Physics
Entanglement and Superposition
Cloning and Key Distribution
Quantum Search and Annealing
Quantum Gates and Factorization

## Slide 4
The story so far
x
y
y = W.x
Essential for regression,
Digital logic
Full Adder (Gates)
NMOS/PMOS
Gate moves Fermi energy
in/out of band
Turns on NMOS
CMOS
Dissipation of energy
Turns on PMOS

## Slide 5
4A. Reversible & Irreversible computing

## Slide 6
Recall why CMOS specifically for inverters
Low power: Once settled, no static current flow
Dynamic power - charging a capacitor to completeness
Charge falling downhill (high V to low V)

## Slide 7
Energy dissipated to charge a capacitor
It’s the energy that cannot
be recovered !!
(Lost irretrievably)

## Slide 8
A capacitor (two metal plates + insulator in between
to hold charge)
C
V0
R
Energy units (eV)  Q x V
Capacitance C: capacity to store charge per volt
C = Q/V [Coulomb/Volts = Farad]
C prop to size: C = [e]A/d [e: Farad/m]

## Slide 9
Energy to charge a capacitor
C
V0
R
C charges to V0 over time T
T = Q/I = CV/[V/R] = RC

## Slide 10
Energy dissipated to charge a capacitor
C
V0
R

## Slide 11
Power dissipated in capacitor
C
V0
R

## Slide 12
Moore
More
than
Moore
More
Without
Moore?
Le roi est Moore, vive le roi
Freq & V
Scaling –
Death of Dennard Scaling
Strained
Si
High-K
Metal Gate
NonPlanar
Gate
No More
ITRS roadmap !
3V
2V
1V
Limited by
Error tolerance
Limited by
Heat
P  CV2f
V
f

## Slide 13
Fairly Large Amt of Energy Wasted
P ~ 80 W at 3 GHz frequency, 2B transistors
~ 130 kW/cm2
E ~ 400 aJ/transistor ~ 2750 eV ~ 110,000 kBT
N ~ 2750 e-s @ ~1 V
Why? Demands on (a) Speed (> 3GHz) and (b) accuracy (1V)
Brain uses ~200,000 more switches, at 1/4th the power by doing this 1.8M times slower.
Also, lower digital accuracy for each switch (~60 mV spikes). But info encoded not in a particular sequence of 0s and 1s, but their relative probabilities (ie, entropy).

## Slide 14
Can we avoid this wasted energy or recycle it?

## Slide 15
Dissipation for unidirectionality  electron falls & sticks
Fall because one side is deeper - Irrespective of speed !
Dissipation due to ‘thud’  Erasing information
drain (output)
source
(Power)
DISSIPATION

## Slide 16
Origin of irreversibility
Erasure of information gives rise to irreversibility
S H A N N O N

## Slide 17
Quantifying knowledge and Dissipation
Dissipation (Energy Loss)
From statistical mechanics
S = kBlnW = kB<ln(1/p)>
= -Si kB(pilnpi)
DF = -TDS
Error
1/W ~ exp[-DF/kBT] (Boltzmann Limit)

## Slide 18
Dissipation in AND (single electron)
DF = -TDS
S = -Si kB(pilnpi)
Si = -4kB(1/4ln1/4)
Sf = -kB(3/4ln3/4 + 1/4ln1/4)
DF = 0.82kBT ~3.2zJ

## Slide 19
What is a zepto?
https://slideplayer.com/slide/8705768/

## Slide 20
How much is a zepto-Joule?
1zJ = 2.39 x 10-24 kcal
1 ATP molecule spends 28kCal/mole in hydrolysis during a phosphorylation reaction.
Divided by Avogadro #, this gives energy burnt by ATP as
4.6 x 10-23 kCal ~ 20 zJ (6X of a 1-electron AND gate)
https://www.expii.com/t/atp-phosphorylation-and-hydrolysis-5775

## Slide 21
Don’t let the electron fall & stick
drain (output)
source
(Power)
NO DISSIPATION ?
By storing information, can we remove dissipation?
DISSIPATION

## Slide 22
Dissipation in Exchange gate
DS = 0
Reminder:
We use base 2 for information entropy
Base e and an extra kB for thermodynamic entropy

## Slide 23
Dissipation in CMOS
DF = -TDS
S = -Si kB(pilnpi)
Si = -kBln1/2
= kBln2
Si = 0
Sf = 0
Sf = 0
When we know where electron sits (“moonwalk”)
When we don’t know where electron sits (usual CMOS)
Initial
Final
Initial
Final
DF = 0, no dissipation
DF = kBTln2 ~ 17.3meV ~ 2.8zJ

## Slide 24
Origin of irreversibility
Erasure of information gives rise to irreversibility (Shannon)
This resetting of entropy actually costs energy!!
We call this ‘dissipation’
Computation
Erasure
Energy kBTln2
Ordered
S = 0
Disordered
S = kBln2
Spend energy to reset
  dE = TdS

## Slide 25
In real life… many electrons
Vt~kBT/q ~ 25 mV needed to avoid backflips.
In practice price of high accuracy!!
V= Vt ln(1/p), need p ~ 10-15 not ½
Many electrons to charge a capacitor to this voltage
For ATP (1.4nm diameter)
C << 1 aF
Q ~ 1e
For 14nm Si FET with 100nm width
C= 1fF for interconnect with FO(4)
Q ~ 6,000e

## Slide 26
Dissipation in CMOS
DF = kBTln2 dissipation
for 2 states
= NkBTln2
for 2N independent states
Magnets
N states are coupled (N  N*)
(act like a giant spin)
TunnelFETs (Seabaugh)
Negative Capacitance (Salahuddin)
MottFETs (Shukla/Datta)
Klein-Tunnel FETs (Ghosh)
NanoElectroMechanical FETs (Liu)
Nonequilibrium Physics (T  T*)
Internal voltage Amplification